## Slide 1
AI / ML · REINFORCEMENT LEARNING CASE STUDY
SMART TRAFFIC SIGNAL CONTROL WITH
OBJECTIVE-MATCHED RL ALGORITHMS
Three Objectives, Each Solved With The Algorithm That Fits It Best
A2C
Emergency Priority
DQN
Fuel · Emission · Safety
PPO
Congestion Reduction
Anantha Narayanan A 2362032
Shaun Joseph Sabu 2362159
Delna Liz Denny 2362060
Presenter — Anantha Narayanan A
01 / 22

## Slide 2
PROBLEM & MOTIVATION
The Urban Intersection Never Stands Still
Dynamic Demand
Vehicle arrival rates and density shift between peak and off-peak periods.
Long Queues
Lanes accumulate more vehicles than the allotted green can discharge.
Waiting Time
Accumulated delay builds across every approach to the intersection.
Fuel & Emissions
Repeated stopping, idling and acceleration raise consumption and emissions.
Emergency Delays
Ambulances and fire engines can be held at a red signal.
Traffic Violations
Red-light and lane violations occur with no signal-side awareness.
WHY CONVENTIONAL SIGNAL CONTROL FALLS SHORT
Fixed-time schedules and hand-designed rule-based strategies assume predictable demand. They cannot re-plan when one lane suddenly develops a long queue, when an accident blocks a lane, or when an emergency vehicle approaches — the timing plan is decided before the traffic ever arrives.
Presenter — Anantha Narayanan A
02 / 22

## Slide 3
PROPOSED APPROACH
One Framework, Three Objective-Matched Algorithms
Rather than forcing every objective through the same algorithm, each agent uses the RL method best suited to the shape of its decision problem.
Traffic
Environment
→
State
→
RL
Agent
→
Signal
Action
→
Reward
→
Learning
Observe → Decide → Control Signal → Observe New Condition → Receive Reward → Learn · one decision every 5–10 s of simulation time
OBJECTIVE 01
Emergency Prioritization
A2C
A continuous trade-off between two competing values (emergency delay vs. normal-traffic delay) — Actor picks the action, Critic scores how good the trade-off is.
Anantha
OBJECTIVE 02
Fuel · Emission · Safety
DQN
A discrete-action, value-based problem with a large replay history to learn from — DQN's Q-value approximation fits directly.
Shaun
OBJECTIVE 03
Congestion Reduction
PPO
Continuously shifting demand needs stable, incremental policy updates — PPO's clipped objective avoids destructive large updates.
Delna
Presenter — Anantha Narayanan A
03 / 22

## Slide 4
SECTION 01 · SLIDES 4–8
01
ANANTHA NARAYANAN A
OBJECTIVE · A2C AGENT
Emergency Vehicle
Prioritization Agent
EMERGENCY PRIORITY · A2C
Develop an objective-focused Advantage Actor-Critic agent that detects approaching emergency vehicles and prioritizes their movement, while maintaining efficient traffic flow for all other road users.
Presenter — Anantha Narayanan A
04 / 22

## Slide 5
EMERGENCY PRIORITIZATION · THE PROBLEM
Every Red Signal Costs Response Time
How can an agent give an emergency vehicle priority without creating excessive congestion for everyone else?
Rapid passage is essential
Ambulances, fire engines and police vehicles must cross intersections without interruption — prioritized without sacrificing efficient flow for everyone else.
Fixed-time signals do not yield
A pre-set schedule can hold an emergency vehicle at red simply because its phase has not arrived.
Delay compounds downstream
Time lost at each intersection accumulates directly into total emergency response time.
Blind priority creates new delay
Clearing one approach at any cost pushes queues and waiting time onto every other direction.
Emergency-priority actions remain constrained by traffic-signal safety rules — minimum green time, yellow transition intervals and maximum green duration. Emergency-vehicle status is therefore built directly into the RL state itself.
Presenter — Anantha Narayanan A
05 / 22

## Slide 6
EMERGENCY PRIORITIZATION · RL FORMULATION (A2C)
State, Action and Reward
STATE
what the agent sees
Emergency vehicle detected / not detected
Emergency vehicle location
Emergency vehicle distance from intersection
Emergency vehicle speed
Queue length in each lane
Waiting time
Current signal phase
Traffic density
Normal traffic flow
ACTIONS
discrete
1
Maintain current signal
2
Extend current green
3
Switch to emergency vehicle direction
4
Reduce current green
5
Restore normal signal operation
REWARD
POSITIVE +
Emergency vehicle delay decreases
Emergency vehicle passes quickly
Normal traffic remains reasonably efficient
NEGATIVE −
Emergency vehicle waits too long
Large queues are created
Excessive delay to normal traffic
Frequent signal switching occurs
R = − α W_e − β Q + γ P_e + δ T
Why A2C? Actor chooses the signal action; Critic evaluates how good the current situation/action is. This fits the emergency trade-off: maximum priority for the emergency vehicle, without completely disrupting normal traffic.
Presenter — Anantha Narayanan A
06 / 22

## Slide 7
EMERGENCY PRIORITIZATION · WORKING SCENARIO
Ambulance Approaching from the North
1
Ambulance detected on North road
State flags emergency presence, location, distance and closing speed.
2
Actor evaluates current phase
N red · E green · W green — the actor weighs priority against the cost to E–W traffic.
3
Actor switches to North
N green · E red · W red — the ambulance is granted a clear path.
4
Critic scores the trade-off
Emergency delay falls sharply; the critic checks the cost imposed on E–W is still acceptable.
5
Ambulance clears intersection
The high-priority episode ends once the vehicle has passed through.
6
Restore normal operation
North does not stay green indefinitely — the agent restores adaptive control to prevent E–W queues building up.
Competing traffic still flowing east–west — the actor weighs its delay before switching, and the critic keeps that trade-off honest.
Presenter — Anantha Narayanan A
07 / 22

## Slide 8
EMERGENCY PRIORITIZATION · EXPECTED OUTCOME
What the Trained A2C Agent Should Achieve
Reduced emergency waiting time
Less time held at red on the emergency approach.
Faster emergency movement
Quicker passage through the intersection.
Improved response efficiency
Lower emergency travel time and delay overall.
Actor-critic priority control
Priority granted from the observed state and critic-evaluated trade-off, not a fixed rule.
Reduced disruption to normal traffic
Other approaches avoid unnecessary added delay — no numerical improvement is claimed yet.
Bounded priority windows
Normal signal operation is restored promptly instead of holding one direction green indefinitely.
“Priority when it matters — without sacrificing overall traffic efficiency.”
Actual values are to be evaluated experimentally in SUMO against a fixed-time baseline. Handing over to Shaun, who covers fuel consumption, emissions and traffic violation detection.
Presenter — Anantha Narayanan A
08 / 22

## Slide 9
SECTION 02 · SLIDES 9–13
02
SHAUN JOSEPH SABU
OBJECTIVE · DQN AGENT
Fuel Consumption, Emission Reduction
& Traffic Violation Detection
EFFICIENCY & SAFETY · DQN
Develop an objective-focused Deep Q-Network agent that reduces unnecessary stops, idling and waiting — thereby reducing fuel consumption and vehicular emissions — while identifying traffic violations.
Presenter — Shaun Joseph Sabu
09 / 22

## Slide 10
FUEL & EMISSIONS · THE PROBLEM
Stop-and-Go Traffic Burns Fuel
Repeated Stopping
Vehicles halting and restarting at every phase change.
Idling in Queue
Engines running while stationary in a backed-up lane.
Unnecessary Acceleration
Hard acceleration after avoidable stops.
CONSEQUENCE
Higher fuel consumption
Higher vehicular emissions
Longer waiting time
Inefficient traffic movement
HOW INTELLIGENT SIGNAL CONTROL CHANGES THIS
Fewer unnecessary stops — vehicles arriving on green do not decelerate to a halt
Shorter idle periods — green time is released where vehicles are actually waiting
Smoother progression — steadier average speed replaces repeated stop-start cycles
→ lower estimated fuel consumption and lower estimated emissions
Presenter — Shaun Joseph Sabu
10 / 22

## Slide 11
FUEL & EMISSIONS · RL FORMULATION (DQN)
State, Action and Reward
STATE
what the agent sees
Vehicle count
Queue length
Average waiting time
Average speed
Number of stops
Current signal phase
Estimated emission level
Violation indicators
ACTIONS
discrete
1
Keep green
2
Extend green
3
Switch phase
4
Reduce green
5
Activate appropriate signal transition
REWARD
POSITIVE +
Vehicles move smoothly
Waiting time decreases
Unnecessary stops decrease
Estimated emissions decrease
NEGATIVE −
Vehicles stationary for long periods
Queue length increases
Unnecessary stops / emissions increase
Unsafe / violation-related events occur
Q(s, a) learned via Deep Q-Network · greedy action = argmax Q(s, a)
Violation indicators enter the state, and violation events enter the reward as a penalty — safety is optimised alongside efficiency, not bolted on afterwards. The discrete action set and rich replay history are exactly what DQN is built for.
Presenter — Shaun Joseph Sabu
11 / 22

## Slide 12
TRAFFIC VIOLATION DETECTION
Monitoring Behaviour at the Intersection
VIOLATIONS MONITORED
Red-light violations
Illegal crossing during red
Lane violations
Unsafe signal-related behaviour
MONITORING PIPELINE
1
Traffic Environment
2
Behaviour Monitoring
3
Violation Indicator
4
Reward Penalty · Safety Metric
SCOPE NOTE
Violation monitoring operates as an additional component connected to the traffic environment. The case study does not specify a particular computer-vision detection model — the indicator is consumed by the state and the reward.
Presenter — Shaun Joseph Sabu
12 / 22

## Slide 13
FUEL & EMISSIONS · WORKING & EXPECTED OUTCOME
From Stop-and-Go to Smooth Flow
Repeated stops,
high waiting, low speed
→
DQN observes
state
→
Adaptive signal
decision
→
Smoother flow,
fewer stops
→
Lower estimated
fuel & emissions
IN PARALLEL: Violation occurs → Detected / flagged → Penalty in reward + monitoring record
EXPECTED OUTCOMES
Reduced unnecessary stops
Reduced idle time
Lower estimated fuel consumption
Lower estimated emissions
Violations detected and flagged
Smoother overall traffic flow
All outcomes are expected results — actual values to be evaluated experimentally in simulation. Handing over to Delna, who covers adaptive traffic congestion reduction.
Presenter — Shaun Joseph Sabu
13 / 22

## Slide 14
SECTION 03 · SLIDES 14–18
03
DELNA LIZ DENNY
OBJECTIVE · PPO AGENT
Adaptive Traffic
Congestion Reduction Agent
CONGESTION REDUCTION · PPO
Develop an objective-focused Proximal Policy Optimization agent that reduces traffic congestion by minimizing vehicle queue lengths and waiting times through adaptive traffic signal control.
Presenter — Delna Liz Denny
14 / 22

## Slide 15
CONGESTION REDUCTION · THE PROBLEM
Equal Green Time for Unequal Demand
FIXED-TIME ALLOCATION
ROAD A
30 vehicles waiting
equal green time
ROAD B
5 vehicles waiting
equal green time
A fixed strategy keeps allocating the same green to both roads, regardless of demand.
• Long queues on the loaded approach
• Increased average waiting time
• Poor utilization of green time
• Reduced vehicle throughput
ADAPTIVE PPO CONTROL
The agent observes the imbalance directly in the state — queue length per lane, arrival rate, phase duration — and dynamically modifies the signal phase instead of following a pre-set plan.
PPO's clipped-update policy gradient lets the agent adjust green allocation gradually and stably as demand shifts through the day, without overreacting to any single noisy observation.
Presenter — Delna Liz Denny
15 / 22

## Slide 16
CONGESTION REDUCTION · RL FORMULATION (PPO)
State, Action and Reward
STATE
what the agent sees
Queue length of each lane
Number of vehicles
Average waiting time
Vehicle arrival rate
Current signal phase
Duration of current phase
Average vehicle speed
Traffic density
ACTIONS
discrete
1
Keep current phase
2
Extend green
3
Reduce green
4
Switch phase
REWARD
POSITIVE +
Decreasing queue length
Decreasing waiting time
Increasing vehicle throughput
Maintaining smooth flow
NEGATIVE −
Long queues
Excessive waiting
Poor throughput
Frequent unnecessary switching
R = − α Q − β W + γ T Queue ↓ + Waiting ↓ + Throughput ↑ = Higher Reward
Why PPO? A policy-gradient actor-critic method that is generally more stable than basic policy-gradient methods, thanks to its clipped surrogate objective — well suited to learning adaptive signal policies under continuously changing conditions.
Presenter — Delna Liz Denny
16 / 22

## Slide 17
CONGESTION REDUCTION · WORKING SCENARIO
Detecting and Correcting an Imbalance
N–S: large queue · E–W: small queue
NORTH–SOUTH
large queue
EAST–WEST
few vehicles
Green time follows the demand, not the clock.
1
PPO agent detects the imbalance in the state
2
Action selected: extend north–south green
3
Queue length decreases as N–S clears
4
Advantage estimate confirms the gain vs. the old policy
5
Positive reward returned
6
Policy updated via PPO's clipped objective
Presenter — Delna Liz Denny
17 / 22

## Slide 18
CONGESTION REDUCTION · EXPECTED OUTCOME
What the Trained PPO Agent Should Achieve
Lower average queue length
Fewer vehicles held waiting per lane.
Lower average waiting time
Less accumulated delay across approaches.
Higher vehicle throughput
More vehicles cleared per unit time.
Better green-time utilization
Green is spent where vehicles actually are.
Reduced congestion
Queues resolve instead of accumulating.
Stable adaptation to changing conditions
PPO's clipped updates respond smoothly as demand shifts through the day.
“Green time allocated by demand — learned stably, not pre-set.”
Expected outcomes — to be evaluated experimentally against a fixed-time controller. That completes the three objectives; we now bring them together.
Presenter — Delna Liz Denny
18 / 22

## Slide 19
TEAM INTEGRATION
Three Objectives, Three Algorithms, One Coordinated System
ANANTHA
Emergency Vehicle
Prioritization
A2C
STATE
Emergency presence, distance, direction, speed
ACTIONS
Switch to emergency direction
REWARD FOCUS
− W_e − Q + P_e + T
SHAUN
Fuel + Emission +
Violation Monitoring
DQN
STATE
Speed, stops, estimated emission, violations
ACTIONS
Appropriate signal transitions
REWARD FOCUS
Smoothness reward − violation penalty
DELNA
Traffic Congestion
Reduction
PPO
STATE
Queue per lane, arrival rate, phase duration
ACTIONS
Keep / extend / reduce / switch
REWARD FOCUS
− α Q − β W + γ T
COORDINATED MULTI-ALGORITHM TRAFFIC SIGNAL CONTROLLER
Each agent contributes state variables, permitted actions and a reward function that fits its own objective — coordinated at the traffic-signal level, not merged into one shared network.
Presenter — Team
19 / 22

## Slide 20
TEAM INTEGRATION
Three Reward Functions, One Behind Each Algorithm
Because each objective is solved by its own agent, each keeps a reward shaped for its own algorithm — rather than one shared equation across all three.
A2C
Emergency Priority
R = − α W_e − β Q + γ P_e + δ T
W_e — emergency waiting time (−)
Q — normal traffic queue (−)
P_e — emergency priority / passage (+)
T — overall throughput (+)
DQN
Fuel · Emission · Safety
Smoothness reward − violation penalty
Smooth flow, falling waits, fewer stops (+)
Falling estimated emissions (+)
Long stationary periods, growing queues (−)
Violation / unsafe events (−)
PPO
Congestion Reduction
R = − α Q − β W + γ T
Q — queue length (−)
W — waiting time (−)
T — throughput (+)
α, β, γ — tunable weights
ONE COORDINATED CONTROLLER BALANCES: Congestion · Waiting · Stops · Emissions · Emergency · Safety
Presenter — Team
20 / 22

## Slide 21
COMPLETE WORKFLOW · EVALUATION
How Each Agent Learns, and How We Will Measure It
A · LEARNING CYCLES
A2C / PPO (Objectives 1 & 3)
1. Observe state
2. Actor selects action, Critic scores value
3. Environment evolves, reward returned
4. Advantage estimated; policy updated on-policy
DQN (Objective 2)
1. Observe state
2. Estimate Q-values for each action
3. Action selected (ε-greedy)
4. Experience stored in replay memory, network updated off-policy
Exploration vs. exploitation governs action selection during training across all three agents; each episode equals one hour of simulated traffic in SUMO.
B · EVALUATION METRICS
Traffic Efficiency
Average waiting time
Average queue length
Vehicle throughput
Average travel time
Environmental
Estimated fuel consumption
CO₂ and other emissions
Number of unnecessary stops
Emergency Response
Emergency waiting time
Emergency travel time
Emergency vehicle delay
Safety / Violations
Detected red-light violations
Other detected violations
Unsafe signal transitions
Baseline for every metric: a conventional fixed-time / rule-based controller — all values to be measured.
Presenter — Team
21 / 22

## Slide 22
INNOVATION · CHALLENGES · CONCLUSION
Where This Goes Next
INNOVATION
Algorithm Matched to Each Objective
A2C for the emergency trade-off — Actor decides, Critic weighs the cost
DQN for discrete, replay-driven efficiency and safety learning
PPO for stable adaptation to continuously shifting congestion
Future extension: coordinate agents further with shared or communicated state — one agent per objective, per intersection, across the network.
CHALLENGES & LIMITATIONS
Known Before We Build
Reward design — weighting objectives per algorithm
Coordinating three independently trained agents
Training time — many episodes across three algorithms
Exploration risk during training
Generalization across intersections
Safety constraints — min green / yellow
Simulation-to-real gap
ANANTHA
Emergency vehicles receive priority via A2C while efficient normal traffic flow is maintained.
SHAUN
Unnecessary stops, fuel consumption and emissions are reduced via DQN while violations are monitored.
DELNA
Traffic congestion is reduced through PPO-based adaptive, queue-aware signal control.
“Three Objectives. Three Algorithms. One Coordinated Intelligent Traffic Control Framework.”
Presenter — Team
22 / 22